| TECHNICAL SPECIFICATIONS OF THE EQUIPMENT FOR 40 POSTS FROM HEALTH |  |  |
| --- | --- | --- |
|  |  |  | PHOTOS just an indication |
| Item No. | Technical specifications | Quantity |  |
| 1 | TABLE REVIEW |  |  |
|  | composed of two parts which one recliner. |  |  |
|  | With minimum thickness 12cm foam mattress, fabric cover plastic type resistant and washable leatherette | 40 |  |
|  | -Maximum range: 200 kg. |  |  |
|  | -Dimensions: L 190 x 70 x h 80 cm |  |  |
| 2 | SCREEN 3 SECTIONS |  |  |
|  | -Isolation of patients in the delivery room or care. -Metal steel frame, supporting a tense opaque fabric. -Stable base. -Dimensions: (L) 60 cm x 3, h 200 cm. | 120 |  |
| 3 | LADDER 2 MARKETS aluminum alloy, anti. Dim: 40 x 20 x 46h cm | 120 |  |
| 4 | SCALE WEIGHS 150 KG PERSON skid |  |  |
|  | · Model dial needle, solid metal construction. | 80 |  |
|  | · Covered deck with a non-slip mat. |  |  |
|  | · Capacity 150 Kg per 100 g |  |  |
| 5 | BALANCE BABY CURSOR 15 KG | 80 |  |
|  | · CE marking. |  |  |
|  | · Table model, clinical type. |  |  |
|  | · Scope 15 kg per 100 gr. |  |  |
|  | · 2 cursors: kg, and gr |  |  |
|  | equipped with a locking system |  |  |
| 6 | BALANCE BABY HAS SUSPENDED DIAL |  |  |
|  | Balance suspendue12 kg per 500 g type Salter, supplied with 5 weighing pants. | 80 |  |
| 7 | FLASHLIGHT PEN | 40 |  |
|  | -For 2 standard batteries 1.5 V |  |  |
|  | -Supplied with 3 bulbs. |  |  |
| 8 | A STAINLESS STEEL PEDAL BIN |  |  |
|  | -Body and cover in stainless steel with gasket. | 160 |  |
|  | -Opening by protected pedal. |  |  |
|  | about 15 to 20 L |  |  |
| 9 | A REFLEX HAMMER | 40 |  |
| 10 | OTOSCOPE | 40 |  |
|  | -Delivered in a box. |  |  |
|  | -Channel 2 batteries 1.5 v battery |  |  |
|  | -Head and independent handle. |  |  |
|  | -5 reusable specula (ear and nasal). |  |  |
|  | -Delivered with 2 bulbs from spare parts and 2 batteries 1.5 v |  |  |
| 11 | Blood pressure monitor + stethoscope |  |  |
|  | -Armbands adhesive velcro adult and child, with pear. | 80 |  |
|  | – Pressure gauge blade, graduated from 0 to 300 mmHg to free needle. |  |  |
|  | -Reset button. |  |  |
|  | Delivered with a PEAR, 1 adult and child armband and 2 rubber tourniquets |  |  |
| 12 | THERMOMETER, CASE |  |  |
|  | medical thermometer | 40 |  |
| 13 | STOOL |  |  |
|  | -Height stool fixed 50 cm. | 80 |  |
|  | -Without folder. |  |  |
| 14 | TABLE OF DELIVERY MANUAL | 80 |  |
|  | -Simple model, easy to clean |  |  |
|  | -Tubular frame in stainless steel or coated with epoxy paint, fixed base, protective rubber caps |  |  |
|  | -Mattress thickness 12 cm minimum width 70 cm, 2 elements, adjustable headrest by Compass: |  |  |
|  | -Fixed height (85 cm approximately in a recumbent position). |  |  |
|  | -Maximum range: 200 kg. |  |  |
|  | -Approximate dimensions: 190 x 70 x 85 cm |  |  |
|  | -Accessories: |  |  |
|  | -1 pair of brackets round diameter 16 cm or support legs |  |  |
|  | -1 Bowl stainless steel receptacle on stainless support |  |  |
| 15 | GYNAECOLOGICAL EXAMINATION TABLE |  |  |
|  | -Examination couch for Gynecology, allowing auscultation of patients in sitting or lying position. | 40 |  |
|  | -Welded steel tubular frame. |  |  |
|  | -Minimum diameter 25 mm, feet protected with rubber tips. |  |  |
|  | -A pair of calipers round diameter 16 cm or legrests. |  |  |
|  | (- Review plan: safe mattress 12 cm minimum thickness foam, fabric cover plastic type simili resistant and washable, composed of three parts including two reclining torso and leg). |  |  |
|  | -Denoise skid base. |  |  |
|  | -Maximum range: 200 kg. |  |  |
|  | -Dimensions: L 190 x 70 x h 80 cm. |  |  |
| 16 | VACUUM DELIVERY MANUAL + 3 SUCTION CUPS |  |  |
|  | · Non-electric vacuum hand pump. | 80 |  |
|  | · Complete with three suction cups soft (40, 50 and 60 mm) equipped with traction chains. |  |  |
|  | · Supplied with a spare jar. |  |  |
| 17 | BALLOON + SET NEW NES TIPS, CHILD, ADULT |  |  |
|  | For adult and paediatric ventilation: | 40 |  |
|  | · Autoclavable. |  |  |
|  | · 1 ball allowing continuous handling, long life, without fatigue. |  |  |
|  | · 1 patient valve with alignment keys. |  |  |
|  | · adult size 2 masks. |  |  |
|  | · 1 large mask size. |  |  |
|  | · 2 pediatric mask. |  |  |
|  | · 1 pocket of enrichment oxygen from the air. |  |  |
|  | 1 silicone hose antistatic, length 200 cm, with 5 nipples of connection has a source d ' oxygen. |  |  |
| 18 | STAINLESS STEEL BASIN | 160 |  |
|  | stainless steel basin for medical bed |  |  |
| 19 | BEAN | 160 |  |
|  | · Bowl-shaped bean in 18/10 stainless steel. |  |  |
|  | · Capacity: 500 ml. |  |  |
| 20 | BOX DRESSINGS |  |  |
|  | 1 box stainless about 200 x 100 x 60 mm | 80 |  |
|  | 1 pair of scissors curved 10 cm |  |  |
|  | 1 pair of scissors straight foams 14 cm |  |  |
|  | 1 straight hemostat Péan 14 cm |  |  |
|  | 1 straight hemostat Kocher 14 cm |  |  |
|  | 1 clip-tweezers claws 14 cm |  |  |
|  | 1 tweezers without claws 14 cm |  |  |
| 21 | BOX INSTRUMENTS DELIVERY OF BASIC | 80 |  |
|  | Stainless steel box comprising: |  |  |
|  | · 2 forceps Kocher 18 cm. |  |  |
|  | · 1 urinary catheter CH12, metal. |  |  |
|  | · 1 pair of scissors with episiotomy 15 cm |  |  |
|  | · 1 pair of scissors straight 18 cm round-tipped. |  |  |
|  | · 1 pair of scissors curved 17 cm. |  |  |
|  | · 2 clips of Pandey. |  |  |
|  | · 1 clamp bar. |  |  |
|  | · 1 door needle Mayo Hegar 16 cm. |  |  |
|  | · 1 spreader of farabeuf. |  |  |
|  | · 1 clip snouts 25cm. |  |  |
|  | · 1 clip Leriche 15 cm. |  |  |
|  | N. B.: |  |  |
|  | The instruments shall be guaranteed for the transition to steam sterilization. |  |  |
|  | The instruments must have the CE marking. |  |  |
| 22 | BOX INSTRUMENT SMALL SURGERY | 40 |  |
|  | · Box dimension aluminum 18 x 8 x 4 cm. |  |  |
|  | · 1 pair straight chisel 14 cm. |  |  |
|  | · 1 fluted probe 14 cm. |  |  |
|  | · 1 needle holder mayo-hegar right of 14 cm. |  |  |
|  | · 1 clip to dissect without claw 14 cm. |  |  |
|  | · 1 clip to dissect with claws 14 cm. |  |  |
|  | · 1 hemostat of Kocher straight without claws 14 cm. |  |  |
|  | · 1 hemostat of Kocher right with claws 14 cm. |  |  |
|  | · 1 clip to splinter. |  |  |
|  | · 1 needle to a foreign body. |  |  |
|  | NOTE: |  |  |
|  | The instruments shall be guaranteed for the transition to steam sterilization. |  |  |
|  | The instruments must have the CE marking. |  |  |
| 23 | SURGICAL BRUSH | 200 |  |
|  | Surgical type brush "Brush/sponge» surgical brushing and anchorage. |  |  |
| 24 | TROLLEY CARE 2 SHELVES | 80 |  |
|  | · Pedestal table in stainless steel. |  |  |
|  | · Stainless steel trays. |  |  |
|  | · Trays dimensions: 90 x 60 cm. |  |  |
|  | · The height of the top of the order of 80 cm. |  |  |
|  | · Swivel wheels. |  |  |
| 25 | CONTAINER INSULATION VACCINES | 80 |  |
|  | -1 vaccine (vaccine cold box) cooler. |  |  |
|  | o capacity: 20-25 L |  |  |
|  | o Conservation of vaccines more than 120 hours at 47 ° C temperature outside. |  |  |
|  | -1 alcohol,-30 to + 50 ° C thermometer. |  |  |
|  | -30 briquettes from cold (icepacks) 0.6 L, |  |  |
|  | adapted to the cooler. |  |  |
|  | vaccines (carrier) of capacity 1.7 L 3-door |  |  |
| 26 | BOWL PLASTIC 15 L | 80 |  |
|  | -Capacity approximately 15 L |  |  |
|  | -Onboard curled. |  |  |
|  | Plastic |  |  |
| 27 | FINGER STERILE | 200 |  |
|  | Lot of 100 sterile microfibre two fingers, sterile |  |  |
| 28 | LAMP GAS SAFETY |  |  |
|  | -Lamp gas protected or plastic glass and transport and hanging handle. | 40 |  |
| 29 | ROUND KNIFE + BLADE | 80 |  |
|  | Rounds 3 and 4 game |  |  |
|  | Set of 5 sterile blades of each of the following numbers: |  |  |
|  | N ° 11 |  |  |
|  | N ° 15 |  |  |
|  | N ° 23 |  |  |
| 30 | POT PRESSURE | 40 |  |
|  | -Tank for sterilization under pressure of instruments or needles. |  |  |
|  | Sterilization on gas, electric stove. |  |  |
|  | Capacity: 9 litres. |  |  |
|  | -Pressure safety valve. |  |  |
|  | -Audible pressure. |  |  |
|  | -Pressure gauge 0-4 bar. |  |  |
|  | -Baskets for needle and syringe and instruments. |  |  |
| 31 | TRAY 240 X 160 X 50 STAINLESS STEEL INSTRUMENTS | 200 |  |
|  | -Stainless steel tray with lid in stainless steel 18/8. |  |  |
|  | -Dimensions: 24 x 16 x 5 cm. |  |  |
| 32 | POISSONNIÈRE STAINLESS STEEL |  |  |
|  | -For sterilisation by boiling. | 40 |  |
|  | -Made of stainless steel. |  |  |
|  | -With handle embossed lid. |  |  |
|  | -Dimensions: 40 x 20 x 10 cm |  |  |
| 33 | SQUEEZE BOTTLE A LIQUOR | 40 |  |
|  | -Squeeze bottle polyethylene flexible, impact resistant, perfectly waterproof. |  |  |
|  | -Neck bottle-shaped, adjustable hose. |  |  |
|  | -Capacity: 500 ml. |  |  |
| 34 | RECHAUD GAS 2 BURNERS + GAS BOTTLE | 40 |  |
|  | -Stove two burner with adaptation of the gas hose nozzle |  |  |
| 35 | MIXED GAS/ELECTRIC REFRIGERATEUR\CONGELATEUR | 40 |  |
|  | Horizontal refrigerator for the storage of vaccines in integrated health posts lack electricity. |  |  |
|  | - Operating gas/electricity |  |  |
|  | -Compression or absorption, CFC-free. |  |  |
|  | -Tropicalized operation, up to 45 ° C outside. |  |  |
|  | -Combining the vaccine storage and freezer for ice pack |  |  |
|  | o storage 20 L capacity |  |  |
|  | o capability on the order of 15 L pack ice freezer |  |  |
|  | -Arranged for stockpiling vaccines and the ice pack |  |  |
|  | -With internal reading control thermometer. |  |  |
|  | -Maximum gas consumption: 0.6 kg/day |  |  |
|  | - Attention: indicate the refrigerator gas consumption |  |  |
|  | - Note : the appliance is used in a first time to operate the gas and possibly a second time on electricity by solar energy. |  |  |
|  | -Spare parts. |  |  |
|  | -Supplied with 2 bottles of gas GM |  |  |
| 36 | SET OF 3 SIZES VAGINAL SPECULUM | 80 |  |
|  | -3 type Cusco vaginal specula games. |  |  |
|  | -Made of stainless steel 18/10. |  |  |
|  | -Non-removable Assembly. |  |  |
|  | Diameters: 16, 30, 38 mm |  |  |
| 37 | STEHOSCOPE PINARD ALUMINIUM | 80 |  |
|  | Pinard aluminum model |  |  |
| 38 | DRUM A DRESSING | 80 |  |
|  | -For sterile and cotton compresses. |  |  |
|  | -Made of stainless steel 18/10. |  |  |
|  | -With sides and lid handle. |  |  |
|  | Diameter of the order of 190 mm, height of the order of 150 mm |  |  |
| 39 | ROD RIBBON | 40 |  |
|  | -Rod tape flexible to attach to the wall 2 m of height. |  |  |
|  | -Wide ribbon down to 50 cm from the ground. |  |  |
| 40 | Beds + mattresses | 80 |  |
|  | Medical beds to a fixed section with feet on skates |  |  |
|  | Epoxy coating |  |  |
|  | Bottomplate in wire mesh |  |  |
|  | Head and footboard to vertical bars |  |  |
|  | Padded mattress with washable and fire-resistant coating |  |  |
|  | Dimensions: 200 X 85 X 50 (h) cm |  |  |
|  | Marking: This Medical |  |  |
| 41 | DOOR SERUM MOBILE 2 HOOKS | 120 |  |
|  | -2 hooks doors stainless steel jars. |  |  |
|  | -Height adjustable up to 200 cm stainless steel column. |  |  |
| 42 | OFFICE - 3 DRAWERS |  |  |
|  | Tubular frame in painted steel. |  |  |
|  | Sheet 8/10 steel. |  |  |
|  | Shelf metal thickness 30 mm, dimensions W 120 x 80 x h 75 cm. | 80 |  |
|  | Side panels and bottom panel in painted steel. |  |  |
|  | Base protector pads. |  |  |
|  | 1 soundproofed metal casing consisting of: |  |  |
|  | 3 sliding on bearings slide storage drawers. |  |  |
| 43 | CHAIR OFFICE | 80 |  |
|  | Assisi 35 x 35 cm and folder curved metal. |  |  |
|  | Seat height: 50 cm. |  |  |
|  | Sheet steel 8/10. |  |  |
|  | Base protector pads. |  |  |
|  | Stackable. |  |  |
| 44 | VISITOR CHAIR | 400 |  |
|  | · Robust, and Stackable chair without armrests. |  |  |
|  | · Frame fixed in epoxy coated metal tubes. |  |  |
|  | · Seat mounted on 4 legs |  |  |
|  | · Seat and backrest with padding in expanded material and fabric coating resistant and washable |  |  |
|  | · Seat dimensions: width and depth of the order of 45 cm. |  |  |
|  | · Seat height: 45 cm. |  |  |
| 45 | CABINET OFFICE 3 SHELVES METAL | 80 |  |
|  | Wardrobe with 2 doors. |  |  |
|  | Sheet steel 8/10. |  |  |
|  | 4 shelves of storage for hanging folders, fixed height. |  |  |
|  | Latches and lock with padlock closure. |  |  |
|  | Supplied with padlock and 2 keys set. |  |  |
|  | Base protector pads. |  |  |
|  | Dimensions: w 100 x d 40 x h 185 cm. |  |  |
|  | The metal surfaces must be scraped before anti-rust treatment and passage of the spray paint. |  |  |
| 46 | CHEST FORT | 40 |  |
|  | Small model |  |  |
| 47 | SHELVING METAL | 40 |  |
|  | -Modular metal shelving steel bottomless. |  |  |
|  | Length 5 m, height 200 cm, depth 40 cm. |  |  |
|  | -Amounts in sheet steel, reinforced. |  |  |
|  | -Metal cross rods for reinforcement of all |  |  |
|  | -Five full metal shelves fixed. |  |  |
|  | -Uploaded by Tablet minimum 140 kg. |  |  |
|  | -The bottom shelf is 5 cm from the ground. |  |  |
|  | -Denoise skid base. |  |  |
| 48 | 1200 X 800 TABLE | 40 |  |
|  | Plateau and fixed metal legs. |  |  |
|  | -Sheet steel 10/10 minimum. |  |  |
|  | -Denoise skid base. |  |  |
|  | -Dimension shelf: L 120 x 80 cm |  |  |
|  | -Height: 75 cm. |  |  |